## Slide 1: AOTA
Asteroidal Occultation Time Analyser

## Slide 2: AOTA is in Occult 4.1.0.14

## Slide 3: and looks like:

## Slide 4: Aim
Create an alternative tool to analyse asteroidal occultation light curves
Focus on measuring the D and R events independently
Handle Limovie & Tangra files
Handle output from integrating cameras
Clear presentation of what is ‘going on’
User friendliness & simplicity – as much as possible!

## Slide 5: Basic methodology
Integrity check, for timing inconsistencies
Putative events identified using cross-correlation analysis
D and R events analysed by fitting a test light curve of varying transition duration, using a χ2 best fit analysis
Uncertainties determined using a Monte Carlo analysis, with noise applied to the test light curve
Apply camera-based corrections to the times

## Slide 6: If no time stamps, set manually

## Slide 7: If start and end time stamps, can fill with calculated rate. But treat with care

## Slide 8: Integrity Check
Highly desirable to have OCR reading of time stamp
Looks for irregularities in time stamp sequence, and for identity in sequential measurements
For integrating cameras, checks that the recorded #frames in each integration interval is constant

## Slide 9: Example video with duplicated frames

## Slide 10: Can check for systematic problems with a Fourier Analysis plot
Bad
Good

## Slide 11: Set integration/binning/normalisation

## Slide 12: Event identification
Test signal extends for the entire recording duration
Sets a minimum cross-correlation level for a possible event
Look for symmetric triangle, straight sides, sharp apex, peak above orange region at bottom, and light curve flat across the bottom.

## Slide 13: Symmetric triangle with straight sides, sharp apex, flat light curve at bottom (see 5 orange bars)

## Slide 14: Cloud event – asymmetric, non-straight sides, no sharp apex, light curve at bottom not flat (see orange bars)

## Slide 15: Can overlay comparison stars
Note how the green line drops at the same time as the cloud event, but not for the occultation

## Slide 16: Can identify up to 5 putative events
Each event can be separately analysed

## Slide 17: Final plot showing fitted light curve and uncertainties

## Slide 18: Some events have two discrete possibilities
Dunham-Agamemnon

## Slide 19: Accuracy visible via χ2 curves
Well-defined event
Poorly-defined event
Small uncertainty on the ‘-’ side, large on the ‘+’ side

## Slide 20: True gradual events have a rise and fall in the plot of χ2

## Slide 21: Disregard anomalous points

## Slide 22: Applies corrections based on camera used

## Slide 23: Can view/save measurement report
AOTA analysis of the file D:\Videos\ofOthers\Metis\20140307-Metis_Pierrefontaines.csv
- analysed on Wednesday, 26 March 2014 at 3:29 AM UTC
- using AOTA v4.1.0.27
Event #1
Event location in video frame ID's
D: 601.0 +1.0/-0.5
R: 914.0 +0.5/-0.5
Event time in UTC
D: 3 8 19.40 ± 0.03
R: 3 8 31.92 ± 0.02
Duration of transition in frames
D: 0
R: 0
SN at event locations
D: 3.0
R: 3.3
===== Camera details =====
Camera : WAT-910BD
Frames integrated : 0
Video system : PAL
==== Measurement info ====
Measurement tool : Limovie
Measured at Field level: False
# Measurements binned : 1
Normalisation : None
Time scale from tool : False
===== end of report ======

## Slide 24: Save plots for sending to others

## Slide 25: Detailed Help file provided, with step-by-step instructions and guidance on interpretation

## Slide 26: Questions?